## Slide 1: Diagnostic X-Ray Production
Lavin: Chapter 4
CTVT: 519-523

## Slide 3: Periodic Table
Notes: Followup:
Atoms vs elements
Atoms – smallest particle of an element – 1 or many
Elements – a basic substance that can’t be simplified (hydrogen, gold, lead, etc.)
Molecule – 2 or more atoms chemically joined together
Compound – a molecule that contains more than 1 molecule

## Slide 4: To review…
As the wavelength of x-ray photons shortens, the energy of the x-ray beam will
  Increase
  Decrease
  Lengthen
  Stay the same

## Slide 5: To review…
As the wavelength of x-ray photons shortens, the energy of the x-ray beam will
  Increase
  Decrease
  Lengthen
  Stay the same
Notes: Indirect proportionality – Shorter wavelength = higher frequency

## Slide 6: Don’t forget…
High frequency = shorter wavelengths = penetrates farther
Lower frequency = longer wavelengths = less penetration

## Slide 7: To review…
Which of the following is a physical property of x-rays?
  Travel in straight lines
  Refract & reflect similar to visible light
  Are visible in the dark
  May be deflected by magnets

## Slide 8: To review…
Which of the following is a physical property of x-rays?
  Travel in straight lines
  Refract & reflect similar to visible light
  Are visible in the dark
  May be deflected by magnets
Notes: Travel straight until interacts with matter, then direction alters
Photons have no electrical charge so are unaffected by magnetic or electric fields
Cannot be refracted or reflected

## Slide 9: To review…
X-rays
  Are measured in meters
  Have longer wavelengths than radio waves
  Have less energy than radio waves
  Are a type of electromagnetic radiation

## Slide 10: To review…
X-rays
  Are measured in meters
  Have longer wavelengths than radio waves
  Have less energy than radio waves
  Are a type of electromagnetic radiation
Notes: Measured in waves
Shorter wavelengths than radio
Higher energy than radio

## Slide 11: Review: Types of Energy
  Mechanical – Energy due to motion or position
      Water, turbines, the earth
  Chemical – Energy from chemical bonds of matter
      Respiration, combustion, explosives, batteries
  Nuclear – Energy released by a nuclear reaction
  Electromagnetic – Energy from a magnetic field produced by the motion of electrical charges
        X-rays, light bulbs, radio waves
  Electrical – Energy made available by the flow of electric charge through a conductor
        Human brain, static electricity, batteries

## Slide 12: Review: Electromagnetic Radiation
Frequency = Rapidity of waves
Notes: Waves:
  Wavelength = length between crests
    Shorter = higher frequency, higher energy
  Frequency – rapidity by which waves hit (hertz)
    Amplitude – Height of wave crest to trough
    Energy & frequency related
      Directly proportional
      Higher = more penetrating power

## Slide 13: To review…
What are the 3 ways an object can be electrified?
Notes: Contact
Friction
Induction

## Slide 14: An object can be electrified by:
  Contact –
      Shocking someone
  Friction – Two objects rub together
  Induction –
      Most important in radiology
      Electrical fields act upon each other without contact
      Used in radiographs, x-ray tubes, transformers, and electric motors
Notes:   Friction – glass & resin
  Induction – Giving rise to something
  Lightning is induction:
  Clouds build up excess electrons when form thunderheads
  Ground is neutral
  Discharge to ground – instant, loud
  Conductors & insulators:
  Conduct easily – water, copper
  Don’t conduct – rubber, plastic, glass

## Slide 15: Electrical circuits require…
Amperage (Milliamperes or mA’s)
    Unit of current
    Regulates electrons to produce x-rays
Resistance (ohms)
    The opposite of current flow
Potential Difference (volts)
    Causes electrons to travel
    Electromotive force – draws electrons from high to low #’s
    Volt – The strength of the potential difference
Notes: Resistance
Diameter impacts
  Small = lots of resistance
  Large = little resistance
Potential difference
Garden hose:
  Empty = no water but lots of potential
  Faucet turned on = moves according to potential difference
  Potential difference is empty hose compared to full

## Slide 16: Learning Objectives: Chapter 4
Understand the mechanical components both inside and outside of an x-ray unit
List & describe the parts of an x-ray tube and trace the creation of an x-ray
Describe the line focus principle and its application in radiography
Define the focal spot, and understand problems that can occur with it
Define the anode heel effect

## Slide 17: Steps in Creating A Radiograph
Getting power to the unit and tube
Heating the tube & producing energy
Converting energy to x-rays
Focusing the beam
Exposure
Development of the latent image
Adjusting settings as needed for a diagnostic radiograph

## Slide 18: Getting Power to the Unit
Power travels from plant to clinic
    Transformers boost power
On-off switch completes the circuit
  Wall switch required by law
Line voltage compensator
  Increases/decreases incoming voltage
Safety precautions in place
  Circuit must be grounded
  Circuit breakers
Notes: Breaking the circuit:
  Burnt out light bulb
    Fine wire that forms the cathode burns out in heat of electron flow
    Circuit is interrupted & light goes out
  Mouse eating through cord – conducts energy & dies
Line voltage compensator
  Standard equipment, usually automatic
Circuit breaker
  Power supply to x-ray unit
  Power reaches it first
  Accepts amperage up to its limit or “rating”
  Works like a fuse except fuse melts
  Hits limit = power interrupter
Grounded
  Electricity needs an alternate route if circuit breaks inappropriately
  Original circuit directed safely to ground wire

## Slide 19: Amperage & Milliamperage
Amperage = unit of current
  Milliampere = 1/1000 ampere
Radiology uses mA to regulate the number of electrons used to produce x-ray photons
Notes: Photon - a tiny particle of light or electromagnetic radiation
Ohm = unit of resistance
Volt = difference in potential

## Slide 20: Getting Power to the X-Ray Tube
3 transformers in an X-ray circuit:
  Autotransformer – Steps up voltage
    Operator selects kV’s to produce radiograph
  High-voltage transformer
    Final step-up to boost voltage
    Boosts voltage from 220 to 125,000 volts
  Filament transformer
    Steps down voltage to the x-ray tube filament
    Filament must reach correct temperature
Notes: Transformers – Receive power from incoming lines & transform power to the x-ray tube
Method of electrification in a transformer is induction

## Slide 21: X-Ray Unit
3 essentials to every unit:
Control Panel
X-Ray Tube
High-Tension Transformer

## Slide 22: Operator Console

## Slide 23: How are X-Rays Produced?
When electrons are slowed or stopped by the atoms of a target area, x-rays are produced.
This target area is inside the x-ray tube.
Once the electrons strike the target area, an x-ray beam is created.

## Slide 24: The X-ray Tube
Tube Housing:
Controls leakage & off-focus radiation
Helps to cool the tube
Notes: Source of x-rays is tube
Interaction of photons & anode generates extreme heat
Ratio of x-rays to heat is 99:1
Housing or envelope usually made of Pyrex

## Slide 25
Let’s break the process down…
Xrays are generated in an xray tube
We need 5 elements to produce xrays
A source of electrons
A way to accelerate the electrons
An obstacle free path
A target
An envelope or tube to provide a vacuum environment

## Slide 26
The Cathode…
Provides a source of electrons and directs the electrons towards to anode.
The cathode has a coiled wire filament that emits electrons when heated. This filament is similar to one found in a light bulb. When the filament is heated electrons are held less tightly and become excited. They can now travel to the anode.

## Slide 27
The amount of energy in the circuit is referred to as milliamperage (mA) This controls the heat of the filament which in turn controls the number of electrons.
Acceleration of the electrons is controlled by the kilovoltage.

## Slide 29
The anode:
A beveled target placed on a cylindrical base.
The base is usually made of copper which acts as a conductor of heat. It draws the heat away from the tungsten target.
There are two types of anodes. Stationary and rotating.

## Slide 30
Small animal installed units use rotating anodes. Portable units use stationary anodes.

## Slide 32: The Line Focus Principle
Describes how electrons interact with anode & change direction
Directs x-rays onto patient
Angles target to create a smaller effective focal spot size
Narrows the beam and increases resolution
Sharpens the final image
Notes: NOT BAD
Typical angle is 11 degrees
15 degrees – widens the beam
< 15 degrees – narrows the beam
Actual vs effective focal spot

## Slide 33: Possible Focal Spot Issues
Off-Focus Radiation:
  “Extrafocal" radiation
  Produced by electrons bouncing off & impacting the anode outside the focal spot
  Collar of lead around tube normally prevents
  Can appear as artifact

## Slide 34: Off-Focus Radiation

## Slide 35: Additional Focal Point Issues
Focal Spot/Heat Bloom:
  Anode gets too hot and is not allowed to cool
  Outer edges of focal spot expand
  Enlarges effective focal spot
  Image loses sharpness
Notes: Focal Spot Bloom: The focal spot size enlarges as milliamperes increase owing to the repulsion of adjacent electrons. This effect is called blooming.
BAD

## Slide 36: Focal Spot Bloom

## Slide 37: The Anode Heel Effect
Causes the Intensity of radiation to be greater on the cathode side of the tube
Bevel of the anode limits x-rays produced on anode side
Place thicker end of patient on the cathode side
  Head usually to right
Notes: NOT BAD – Can be used

## Slide 38: The Exposure Switch
The final step in producing an x-ray
Sets the events in motion
Usually 2-stage
  Wait for ready signal
  Can be hand or foot switch
  1st stage activates the rotor & transformers
  2nd Stage activates the exposure through the tube
Be familiar with the noises
  They may scare your patient – be ready!
  Sound of boiling liquid is bad – tube could rupture
Notes: “Dead man” safety factor
Meet again at 10:05 for group activity
Beginning to look at radiographs!

## Slide 40: What makes a good radiograph?
“Gracie”
Notes: HBC/Compassion fatigue?
Diagnostic:
  Correct anatomy
    Symmetry
    Landmarks
  Correct view
  Correct density
  Correct contrast
  Diagnostic
Danger of non-diagnostic?
  Treatment errors
  Retakes
    Increased exposure
    Fractious animals
    Time
    Supplies
    Equipment wear

## Slide 41: Why is radiology important?
Allows us to visualize inside an animal in a non-invasive way…
      Diagnosis
      Treatment
      Guidance
Notes: Diagnosis
  Bones
  Growths
  Tissues
  Results of treatment
Treatment
  Ultrasound - High frequency sound waves
    Break up blockages (kidney stones)
  Radiation therapy - cancer
Guidance
  Guidance of instruments through the body
    Fluorescent markers
    Ultrasound & MRI

## Slide 42: What makes a diagnostic radiograph?
Notes: Diagnostic:
  Correct anatomy
    Symmetry
    Landmarks
  Correct view
  Correct density
  Correct contrast
  Diagnostic
Danger of non-diagnostic?
  Treatment errors
  Retakes
    Increased exposure
    Fractious animals
    Time
    Supplies
    Equipment wear

## Slide 43: Questions To Ask Yourself…
Is this the view ordered by the DVM?
Is the correct body part clearly in view?
Is the body aligned properly?
Is the radiograph dark enough, but not too dark?
Are the differences between body structures clear?
Are there obvious artifacts?
Notes: Diagnosis
  Bones
  Growths
  Tissues
  Results of treatment
Treatment
  Ultrasound - High frequency sound waves
    Break up blockages (kidney stones)
  Radiation therapy - cancer
Guidance
  Guidance of instruments through the body
    Fluorescent markers
    Ultrasound & MRI

## Slide 44: Group Assignment: What Makes a “Good” Radiograph?
Divide into groups
Discuss each radiograph as a group:
  Is there a clear body part of interest, and what is it?
  Can you tell the species?
  Is it a “good” or diagnostic radiograph?
  Does it appear to be OK as is, or should something be changed?
  Any other observations?
Turn in your findings as a group
  Include your names & the date
  **We’re just looking for general observations at this point**

## Slide 45: What’s Next?
Tomorrow: Film imaging
  Lavin: Chapter 5
  CTVT: 532-536
      Image formation with screen systems
      through (and including)
      Grids
Friday: Technical factors & technique charts
  Lab Groups due
  Seating chart final
Test next Wednesday

## Slide 47: To review…
To produce x-rays, a great deal of energy in an x-ray tube is converted to heat. The ratio of heat generated to x-ray production is considered to be
  1%:99%
  99%:1%
  50%:50%
  75%:25%

## Slide 48: To review…
To produce x-rays, a great deal of energy in an x-ray tube is converted to heat. The ratio of heat generated to x-ray production is considered to be
  1%:99%
  99%:1%
  50%:50%
  75%:25%
Notes: Temps in excess of 2000 degrees C are required to loosen electron binding energy

## Slide 49: To review…
During an exposure, electrons in the x-ray tube travel from the
  Anode to the cathode
  Anode to the target
  Cathode to the anode
  Cathode to the filament

## Slide 50: To review…
During an exposure, electrons in the x-ray tube travel from the
  Anode to the cathode
  Anode to the target
  Cathode to the anode
  Cathode to the filament

## Slide 51: The X-ray Tube
Tube Housing:
Controls leakage & off-focus radiation
Helps to cool the tube