## Slide 1: Film Imaging
Lavin: Chapter 5
CTVT: 532-536
Notes: Ronnie’s snood
A tubular neck scarf. In the most common form the headgear resembles a close-fitting hood worn over the back of the head. A tighter-mesh band may cover the forehead or crown, then run behind the ears and under the nape of the neck.

## Slide 2: Let’s Review…
List 3 essential pieces of equipment found in every x-ray unit…
Notes: 3 essentials to every unit:
Control Panel
X-Ray Tube
High-Tension Transformer

## Slide 3: X-Ray Unit
3 essentials to every unit:
Control Panel
X-Ray Tube
High-Tension Transformer

## Slide 4: Label the Parts of an X-ray Tube…
Notes: A – Stator B – Bearing C – Tungsten Anode
D – Envelope E – Filament F – Electron Beam
G – Neck & Base H – Rotor I – Armature
Cathode?
Anode?
Path of the electrons
Place where x-rays start
Target Window
What is the space charge?

## Slide 5: The X-ray Tube
Tube Housing:
Controls leakage & off-focus radiation
Helps to cool the tube
Notes: Source of x-rays is tube
Interaction of photons & anode generates extreme heat
Ratio of x-rays to heat is 99:1
Housing or envelope usually made of Pyrex

## Slide 6: In Review…
What are the 2 types of anodes, and what distinguishes them?
Notes: Rotating anode units – Small animal units
Produces higher quality x-rays
Rotation apparatus must be high quality & perfectly balanced
Stationary anodes – Portable units often used for large animal or dental
Limited application for abdomen/thorax because not powerful enough beam for thicker body parts

## Slide 7: What is the purpose…
Of the CATHODE:
Of the ANODE:
Notes: Of the CATHODE:
Houses the filaments
Generates heat to create cloud of electrons
Focuses electrons to target
Of the ANODE:
X-rays are produced at focal spot
Mechanically supports the electron target
Dissipates heat
Electrical conductor
Completes the circuit
Receives electrons and transmits them back to generator

## Slide 8: What is the purpose…
Of the CATHODE:
Houses the filaments
Generates heat to create cloud of electrons
Focuses electrons to target
Of the ANODE:
X-rays are produced at focal spot
Mechanically supports the electron target
Dissipates heat
Electrical conductor
Completes the circuit –
  Receives electrons and transmits them back to generator
Notes: Dissipates heat along the stem and by rotating to change where photons are focused

## Slide 9: Review: What Does This Represent?
Notes: The Line Focus Principle: Describes how electrons interact with anode & change direction

## Slide 10: The Line Focus Principle
Describes how electrons interact with anode & change direction
Directs x-rays onto patient
Angles target to create a smaller effective focal spot size
Narrows the beam and increases resolution
Sharpens the final image
Notes: NOT BAD
Typical angle is 11 degrees
15 degrees – widens the beam
< 15 degrees – narrows the beam
Actual vs effective focal spot

## Slide 11: What Does This Represent?

## Slide 12: Possible Focal Spot Issues
Off-Focus Radiation:
  “Extrafocal" radiation
  Produced by electrons bouncing off & impacting the anode outside the focal spot
  Collar of lead around tube normally prevents
  Can appear as artifact

## Slide 13: What Does This Represent?

## Slide 14: The Anode Heel Effect
Causes the Intensity of radiation to be greater on the cathode side of the tube
Bevel of the anode limits x-rays produced on anode side
Place thicker end of patient on the cathode side
  Head usually to right
Notes: NOT BAD – Can be used

## Slide 15: To review…
To produce x-rays, a great deal of energy in an x-ray tube is converted to heat. The ratio of heat generated to x-ray production is considered to be
  1%:99%
  99%:1%
  50%:50%
  75%:25%
Notes: B
Temps in excess of 2000 degrees C are required to loosen electron binding energy

## Slide 16: Diagnostic?
Notes: Marsha’s baby

## Slide 18: Learning Objectives: Chapter 5
Identify cassettes, screens, and film, and understand how they work together to create an image
Understand latent image formation
Understand correct storage and care of film, cassettes, and intensifying screens

## Slide 19: Producing Radiographs
The image receptor receives the produced x-rays and produces the actual image.
Receptor components in film-based imaging:
    Cassette/film holder
    Intensifying Screen
    Film

## Slide 20: The X-Ray Cassette
A film holder designed to contain a pair of intensifying screen and one sheet of film
Sturdy and unbendable
Radiolucent front (nearest the patient) & leaded back (away from the patient)
Must hold film securely
Must latch securely
Notes: Radiolucent - permitting the passage of radiant energy, such as x-rays, with little attenuation, the representative areas appearing dark on the exposed film.
Radiopaque - Not allowing the passage of x-rays or other radiation

## Slide 21: The Cassette
Designed to sandwich x-ray film with good contact between two intensifying screens.
  Intensifying screens: Fluorescent sheets of plastic that convert x-ray radiation into visible light, creating a latent image on the film.
Film is processed to convert a latent image to a visible image.
Notes: Latent image:
An invisible image produced by the exposure to light of a photosensitive material such as photographic film
When photographic film is developed, the area that was exposed darkens and forms a visible image.
Physically - A latent image is a small cluster of metallic silver atoms formed in or on a silver halide crystal due to reduction of interstitial silver ions by photoelectrons (a photolytic silver cluster).
Contains foam rubber

## Slide 22: Poor Film/Screen Contact
Notes: Structures are visible but appear fuzzy

## Slide 23: The Cassette
A rigid film holder that holds x-ray film and intensifying screens in close contact
Made of light-tight materials to prevent unwanted exposure, still allow penetration of x-rays
Originally cassettes were made with cardboard, but could not be reused.
Different forms today include aluminum, polycarbonate, magnesium, and carbon fiber.

## Slide 24: Cardboard Film Cassette (Historical)

## Slide 25: Film Cassette (Today)

## Slide 26: The Cassette
Hinges and catches form a light-tight seal
Back of cassette:
  Lined with lead material to absorb backscatter
  Heavier construction than the front
Inside the cassette:
  Both sides lined with felt or foam pressure pads to ensure close contact of the film to the intensifying screens

## Slide 27: The Cassette
Sizes vary.
  Correspond to screen and film sizes.
    Cost varies as well.
Film is sold in specific sizes to match the cassette size

## Slide 28: Lead Blocker
Found in corner of cassette
Prevents irradiation of the part of the film necessary for identification.
Be careful not to have any important body part obscured

## Slide 29
Lead Blocker
Label the film over the part of the cassette shielded by the lead blocker…

## Slide 30: Lead Blockers
The cassette can be divided into four quadrants, using lead protective items.

## Slide 31: Film Cassette/Intensifying Screens

## Slide 32: Intensifying Screens
Made of layers of tiny crystals bonded on plastic and covered by a protective coating
  Crystals emit light after exposure to x-rays
Purposes:
  Reduces the amount of radiation required to produce a diagnostic radiograph
  Enhances contrast
The screens in an x-ray cassette sandwich the film.
Screens are rated by how fast the x-rays are converted to light by the phosphors in its layers.

## Slide 33: Intensifying Screens
Reduces mAs needed, so…
  Decreases radiation dose to the patient
  Reduces the chance of motion on the radiograph
Three “musts” for efficiency of screen materials:
  High level of x-ray absorption
  High x-ray to light conversion
  Little or no “afterglow once radiation has ceased

## Slide 34
Intensifying Screens
Only 5% of exposure results from ionization of x-rays. The remainder is due to light emitted from intensifying screens.

## Slide 35
X-Ray Film
X-ray film is made of a suspension of light & x-ray sensitive silver bromide granules in a gelatin emulsion coated over a polyester base
2 categories:
  Screen – Sensitive to wavelengths emitted from intensifying screens
    Requires less exposure
  Non-screen – Designed for direct exposure
    Needs extra-long exposure times
X-ray film has virtually infinite resolution

## Slide 36
Layers of X-Ray Film
Film Base – Holds the emulsion of the film
Film Emulsion – Contains the photosensitive silver-based products in a gelatin layer, allows processing chemicals to infiltrate
Super coat – Tough, protective coating of hard gelatin
Adhesive layer – Very thin layer that connects emulsion & film base
Notes: Emulsion - A photosensitive coating, usually of silver halide grains in a thin gelatin layer, on photographic film, paper, or glass.
Latent image is formed within emulsion when x-rays and light activate the silver particles in the film emulsion
Forms lattice network of silver halide particles
Latent image is fragile

## Slide 37: Cassette Care
Both the cassette and the screens should be kept clean
  Commercial cleaners are available
  Clean cassettes on a regular basis with mild soap/water.
    Clean screens with distilled water
  Clean exterior & interior at least once monthly.
Number the cassettes so problems can be easily identified

## Slide 38: Cassette Care (cont.)
Handle with care
  Common damage includes: dropping, body fluids
  Cassette storage:
    Upright away from radiation
    Do not stack
    Should be loaded and ready to use
    Avoid humidity & dust
  Film storage:
    Boxes on edge and protected from light

## Slide 39: Plans for today & tomorrow…
Today: Lab Tours
  Should free time for a review next week…
Tomorrow: Producing the Image
  Lavin: Chapter 6
  CTVT: 529-532
    Exposure factors through Formulation of a Technique Chart