## Slide 2: Radiographic Concerns: Forelimb
Field of view:
  Long bones – Include proximal & distal joints
  Joints – Include 1/3 of the bones proximal & distal
Most projections via tabletop
  Collimate tightly
Can split image:
  Point toes the same direction
  Collimate & shield other side
R Mediolateral Carpus

## Slide 3: Radiographic Concerns: Forelimb (cont.)
Non-manual restraint (where possible)
Place label at:
  Lateral view - Dorsal or cranial aspect
  Other views – Lateral aspect
Keep bone parallel to cassette and beam perpendicular
Increase exposure factors if splints/casts in place
R Mediolateral Tarsus

## Slide 4: The Forelimb: Radiographic Anatomy
Shoulder Joint – Mediolateral & CaCr
Scapula – Mediolateral & CaCr
Humerus – Mediolateral, CaCr, and CrCa
Elbow – Mediolateral, CrCa
Radius/Ulna – Mediolateral, CrCa
Foot – Mediolateral, DPa
Notes: Why caudocranial? Closer to cassette
Distal to humerus – CrCa becomes preferable

## Slide 5: Shoulder Joint (Mediolateral View)
Notes: Notice:
T-shape
Non-manual restraint
Central ray at area of interest
Careful collimation

## Slide 6: Shoulder Joint (Mediolateral View)
Area of interest closest to cassette
Extend affected leg cranially & ventrally
Opposite leg pulled out of way
Arch head & neck dorsally
Hind limbs in natural position
Don’t over-rotate thorax
Head & limbs make a “T”
Borders: Proximal 1/3 of humerus & scapula
Notes: Avoid superimposition of structures over shoulder.
If over-rotate - - Shoulder may lift off cassette.

## Slide 7: Shoulder & Scapula (Caudocranial View)
(Same positioning for humerus)

## Slide 8: Humerus (Mediolateral View)
*Positioning is identical to scapula

## Slide 9: Humerus (Mediolateral View)
Lateral recumbency with affected leg down
Affected leg is extended forward
  Opposite leg drawn back
Head and neck extended dorsally.
Larger dogs may need 2 views
  Elbow/shoulder may differ in density
Center ray at mid-shaft
Borders – 1/3 bone proximal to shoulder & distal to elbow

## Slide 10: Humerus (Caudocranial View)
  Same positioning as for shoulder/scapula
  Be aware of distortion since forearm is away from cassette

## Slide 11: Elbow (Mediolateral Extended View)
  Move head & neck dorsally
  Extend other limb caudally
  Affected elbow joint is in 120-degree extended position
  Maintain symmetry of structures with small foam pad under distal region of affected limb

## Slide 12: Elbow (CrCa View)
* Same positioning for other CrCa views (with different borders)
Foam pad under unaffected limb
Pull head away from affected limb
Center ray on center of humeral condyles
Borders – 1/3 of bone proximal & distal
Symmetry is essential

## Slide 13: Radius & Ulna (Mediolateral View)
  Same as for extended elbow view (with different borders)
  Place foam under the humerus & cranial thorax to maintain alignment
  Make sure cassette is large enough to include correct borders
  Measure at mid-shaft to minimize over-exposure

## Slide 14: Radius & Ulna (CrCa View)
  Positioning as for CrCd elbow view (with different borders)
  Measure at mid-shaft of bone

## Slide 15: Carpus (Mediolateral Hyperflexed View)
Lateral recumbency
Hyperflex carpus
Helps evaluate carpal
    joint laxity
Borders – Proximal third of metacarpus to distal third of radius/ulna
Notes: Use tape or paddle to hyperextend - Do not extend carpus beyond normal range of motion

## Slide 16: Foot (Mediolateral View)
  Separate digits with tape (cotton isn’t as effective)
  Measure & center primary beam at site of interest
  Borders – Proximal 1/3 metacarpus to distal 1/3 R/U
  Cassette can be split – point toes in same direction

## Slide 17: Foot (Dorsopalmar View)
Notes: Weird about view?

## Slide 18: Hind Limb: General Considerations
Anatomy (Pelvis):
  Half of femoral head should be in the acetabulum
  Femoral heads should be rounded and smooth
  Femoral neck should be smooth with no remodeling
Views (2):
  Dorsal recumbency for pelvis (V/D) and femur (CrCa)
  Sternal recumbency for distal hind limb (CdCr)
Notes: CrCd Tib/Fib

## Slide 19: Hind Limb Terminology
Dorsal recumbency: Used for proximal hind end
Sternal recumbency: Used for distal rear limbs

## Slide 20: The Pelvis: Standard Positions
Ventrodorsal
Lateral
Ventrodorsal Frog-Leg

## Slide 21: Femur – Standard Views
Mediolateral
Craniocaudal

## Slide 22: Femur: Mediolateral View
Positioning:
  Flex unaffected limb & pull back
  Extend affected limb & secure
  Ensure full limb is in view
  Differences in thickness may require 2 views
  Femoral head towards cathode
  Secure other body parts first
Notes:     Support with a cord or rope
    Use sandbags as needed

## Slide 23: Stifle – Standard Views
Mediolateral
Caudocranial
(Sternal recumbency)

## Slide 24: Stifle: Caudocranial View
Positioning:
  Sternal recumbency
  Unaffected limb flexed near body
  Affected limb rests on patella
    Raising unaffected limb may help

## Slide 25: Tibia & Fibula – Standard Views
Mediolateral
Caudocranial
(Sternal recumbency)

## Slide 26
Tarsus & Foot – Plantarodorsal